## Slide 1: EQV Demo Vehicle Architecture
Heiko Wilken / Stefan Maier

## Slide 2: Agenda
01 | Component Overview
02 | Communication Architecture
03
04
05
06
07
08
12
11
10
09

## Slide 3
01
Component Overview

## Slide 4: Demo CAR Components Architecture
The Demo Car is stacked with different system components from ZF-Liftec product portfolio (see examples at: https://zf-lifetec.com/products). Each seat contains at least:
  ACR8/ACR8s (Active Controlled Reatractor)
  ABL/ACB (Active Buckle Lifter/Active Controlled Buckle) with ISB (Illuminated Seat Buckle)
  HB 2.0 (Heated Belt)
For more detailed information of the components see next slide
All this components are controlled via Rapid Prototyping Units
  Adcos Panther
  Adcos Puma PTM
  Nvidia Jetson Orin
&

## Slide 5: DEMo CAR Architecture
Backbone
Zero-G
Seat Requirements
Full electrical adjustable
Seat heat sensor
Seat position sensor
Rotation and Uplift mechanism
TOF camera
Occupant Monitoring and Classification
(SIMI)
48V
Driver Seat with
ACR8 & WMS
IR Belt
ISB
Weight Sensors
SWS with HOD and HMI
Passenger Seat with
48V ACR with WMS
Heatbelt
ISB
Weight Sensors
2. Row Reverse Seats with
ACR8.S with WMS
E-Locking
Heatbelt
ACB Buckle with ISB
Rotation Sensor
Zero G Seat with
ACR8.S with WMS
E-Locking
Heatbelt
ACB/ABL Buckle with ISB
Reversible Seat Ramp
Tablet for control and visualization
Backbone with
Rapid Prototype Boxes
Data Loggers
Sound Generator with Loudspeaker
Airbag Deployment Simulator
Router and Power Supply
IR
Radar
TOF
Radar
Child Presence
(SIMI)
Steering Wheel with HOD and HMI - Demonstrator for Vitality and Vibration Motor and
new IRS deployment
Advanced Occupant Safety Strategy for Adaptive Restraint with Loudspeaker
(IRS Firing)
2025-03-20 | Heiko Wilken | ZF LIFETEC
Seat Ramp

## Slide 6
02
Communication Architecture

## Slide 7: Communication Architecture
The main data exchange between the rapid prototyping units and the Car-PC should be CAN
  ZF-Liftec will define a DBC-File for the CAN Bus definition and signal conversion rules.
  First draft of the Panther to CAR-PC interface can be seen in the provided excel sheet (DRAFT).
In case of direct ECU/ rapid prototyping unit parameterization XCP Protocoll via Ethernet can be used.
  ZF-Liftec will ship A2L Files where the IP-Adresses and Ports of each ECU are defined as well as parmeters and measurement variables.
For exchange of video streams the same Ethernet connection can also be used to transfer the video stream
  SIMI (100% subsidiary company) will provide details for it when necessary.

## Slide 8: DEMo CAR Bus Communication
2026-02-16 | RDUE2-Algo Team | ZF LIFETEC
THINK
Panther
ACT
PUMA PTM
Driver
ACT
PUMA PTM
Passenger
ACT
PUMA PTM
Seat RL2
Rear normal
ACT
PUMA PTM
Seat RL1 Rear reverse
CAN
Vehicle CAN
CAN
Zero G Seat
CAN
Adaptive
Restraint
Crash Visualization and Acustic
Simi
DMS and OMS
(ORIN/Jetson Nvidia)
Visualization and Control Panel Server
CAR-PC
CAN
Digital or Analog Wired
Reversible
Seat Ramp
Tablets
ACT
PUMA PTM
Seat RR1
Data Logger
eLocking ECU
CAN
DBC
DBC
Crash Sensor FR
Crash Sensor FL
DBC
Body CAN
DBC
CAN / LIN from single IEE-ECUs (installed under the Seats)
LTS
SIMI
RDU
Responsibility

## Slide 9: Ethernet Communication Setup (draft)
THINK
Panther
ACT
PUMA PTM
Driver
ACT
PUMA PTM
Passenger
ACT
PUMA PTM
Seat RL2
ACT
PUMA PTM
Seat RR1
ACT
PUMA PTM
Seat RR1
Switch
Router
CAR-PC (Visualization)
Nvidia Jetson (SIMI)
ETH Cat XX
ETH Cat XX
ETH Cat XX
ETH Cat XX
ETH Cat XX
ETH Cat XX
ETH Cat XX
ETH Cat XX
LTS
SIMI
RDU
Responsibility

## Slide 10: DEMo CAR system Architecture – IEE Components
Responsibility
2026-03-13 | RDUE2-Algo Team | ZF LIFETEC
THINK
Panther
CAN
LIN
JETSON
SIMI Algorithm
CAR-PC
Ethernet
DBC
ACT
PUMA PTM
Driver
ACT
PUMA PTM
Passenger
ACT
PUMA PTM
Seat RL2
ACT
PUMA PTM
Seat RR1
ACT
PUMA PTM
Seat RR1
IEE Seatmat
Driver
IEE Seatmat
Passenger
IEE Seatmat
Seat RL2
IEE Seatmat
Seat RR1
IEE Seatmat
Seat RR1
IEE ECU
IEE ECU
IEE ECU
IEE ECU
IEE ECU
Ethernet
Responsibility by IEE
Responsibility by RDU
Responsibility by SIMI
IEE Radar
LDF
LDF
DBC
Responsibility by LTS
LIN

## Slide 11
CONTACT
Name Surname Job title 0123 - 456 789 0 n.surname@zf.com